## Slide 1: Overview of Digital Elevation from Shuttle Radar Topography Mission (SRTM) and Advanced Spaceborne Thermal Emission and Reflection Radiometer (ASTER)

## Slide 2: Learning Objectives
By the end of this presentation, you will be able to:
Understand SRTM and ASTER Digital Elevation Modeling (DEM) data
Access DEM for Flood Management Applications

## Slide 3: Outline
Overview of SRTM and ASTER DEM Data
SRTM and ASTER DEM Data Access
  Global Data Explorer (GDEx)
  Consultative Group for International Agricultural Research (CIGAR)
Demonstration of GDEx

## Slide 4: Overview of SRTM and ASTER DEM Data

## Slide 5: What is SRTM?
A c-band (5.6 cm) radar mission
On NASA Space Shuttle Endeavour
Completed February 2000
176 orbits around Earth in 11 days
Acquired digital terrain elevation data of all land between 60oN- 56oS latitude
  ~80% of Earth’s total land mass
http://www2.jpl.nasa.gov/srtm/mission.htm
Image Credit (Right): DLR
Notes: To acquire topographic (elevation) data, the SRTM payload was outfitted with two radar antennas. One antenna was located in the shuttle's payload bay, the other on the end of a 60-meter (200-foot) mast that extended from the payload pay once the Shuttle was in space

## Slide 6: SRTM Digital Terrain Data
SRTM used interferometry to gather topographic (elevation) data
Interferometry:
  two radar images of the same area are taken from different views
  the difference in the two images determines the height of the surface in the digital elevation model (DEM)
http://www2.jpl.nasa.gov/srtm/instr.htm
Based on a JPL graphic: http://www2.jpl.nasa.gov/srtm/instrumentinterferometry.html
Transmitted Wave
Received Wave
Radar signals being transmitted and received on the SRTM mission (not to scale)
baseline
Notes: To acquire topographic (elevation) data, the SRTM payload was outfitted with two radar antennas. One antenna was located in the shuttle's payload bay, the other on the end of a 60-meter (200-foot) mast that extended from the payload pay once the Shuttle was in space

## Slide 7: NASA SRTM Version 3.0 (SRTM Plus)
As of 2015, terrain data are available at 1 arc second or 30 m spatial resolution
Eliminated voids in SRTM data by filling with:
  ASTER GDEM2
  USGS GMTED2010
  USGS National Elevation Dataset (NED)
mage Credit: WWF
Notes:   GMTED2010 (Old GTOP30)
New data sources include global Digital Terrain Elevation Data (DTED�) from the Shuttle Radar Topography Mission (SRTM), Canadian elevation data, Spot 5 Reference3D data, and data from the Ice, Cloud, and land Elevation Satellite (ICESat). GMTED2010 provides a new level of detail in global topographic data. The GMTED2010 product suite contains seven new raster elevation products for each of the 30-, 15-, and 7.5-arc-second spatial resolutions and incorporates the current best available global elevation data.

## Slide 8: Advanced Spaceborne Thermal and Reflection Radiometer (ASTER)
Onboard Terra
  Polar orbiting satellite launched Dec 1999
Spatial Coverage and Resolution
  Global
  Swath Width: 60 km
  Spatial Resolution Varies:
    15 m
    30 m
    90 m
http://asterweb.jpl.nasa.gov/
Images of New Zealand glaciers in 1990 (Landsat, top) and 2017 (ASTER, bottom)

## Slide 9: Advanced Spaceborne Thermal and Reflection Radiometer (ASTER)
Spectral Bands
  14 bands (visible to thermal IR bands)
    Bands 1-3: 15 m (VNIR)
    Bands 4-9: 30 m (SWIR)
    Bands 10-14: 90 m (TIR)
Status alert: ASTER SWIR data acquired since Apr 2008 not usable
http://asterweb.jpl.nasa.gov/

## Slide 10: ASTER Global Digital Elevation Model (GDEM V2)
A joint product developed and by NASA and the Ministry of Economy, Trade, and Industry (METI) of Japan
Uses ASTER VNIR stereo pair images to derive DEM
GDEM version 2 is available since 2011, based all available ASTER stereo images
http://asterweb.jpl.nasa.gov/gdem.asp
Covers land surfaces between 83°N and 83°S and is composed of 22,600 1°- by -1° tiles of 30 m resolution
Notes: “GDEM Version 2 shows significant improvements over the previous release. However, users are advised that the data contains anomalies and artifacts that will impede effectiveness for use in certain applications. The data are provided "as is," and neither NASA nor METI/Japan Space Systems (J-spacesystems) will be responsible for any damages resulting from use of the data.”

## Slide 11: SRTM and GDEM2 Accuracy
Based on comparison with 18000 geodetic points over the U.S.
“…the GDEM validation team recommends the release of the GDEM2 to the public, acknowledging that, while vastly improved, some artifacts still exist which could affect its utility in certain application” - ASTER GDEM team [ https://pubs.er.usgs.gov/publication/70005960 ]
DEM | Minimum | Maximum | Mean | Standard Deviation | RMSE | LE95
GDEM2 | -137.37 | 64.80 | -0.20 | 8.68 | 8.68 | 17.01
NED | -46.21 | 16.42 | -0.33 | 1.81 | 1.84 | 3.61
SRTM | -28.67 | 28.58 | 0.73 | 3.95 | 4.01 | 7.86
GDEM1 | -127.74 | 105.41 | -3.69 | 8.58 | 9.34 | 18.31
Results from the CONUS absolute vertical accuracy assessment (in meters)
Notes: ASTER Global Digital Elevation Model Version 2 - summary of validation results (2nd ed., Federal Government Series, Rep.). (2011). Retrieved from https://pubs.er.usgs.gov/publication/70005960

## Slide 12: SRTM and GDEM2 Accuracy
DEM data accuracy depends on location and land cover categories
Tighe, M. L., & Chamberlain, D. (2009). Accuracy Comparison of the SRTM, ASTER, NED, NEXTMAP USA Digital Terrain Model Over Several USA Study Sites. In ASPRS/MAPPS 2009 Conference Proceedings. San Antonio, TX. Retrieved from http://www.asprs.org/a/publications/proceedings/sanantonio09/Tighe_2.pdf
Land Cover | SRTM (rmse m) | GDEM2 (rmse m)
Grass & Shrub | 12.36 | 16.6
Deciduous | 25.49 | 20.79
Evergreen | 24.76 | 22.23
Mixed | 18.81 | 10.03

## Slide 13: DEM Applications
Useful for mapping hazardous terrain
Calculate:
  slope and aspect
  catchment area
  forest canopy height
Models:
  runoff
  stream networks
  landslides
USGS HydroSHEDS

## Slide 14: SRTM DEM Application in Flood Modeling
The Global Flood Monitoring System (GFMS) uses HydroSHEDS* derived from SRTM DEM is used in for identifying river networks for routing models
*(http://hydrosheds.org/)
Wu et al., Real-time Global Flood Monitoring and Forecasting using an Enhanced Land Surface Model with Satellite and NWP model based Precipitation. GFMS. http://flood.umd.edu/GFMS_conference.pdf

## Slide 15: SRTM and ASTER DEM Data Access

## Slide 16: Global Data Explorer (GDEx)
Seamless data viewer that provides access to multiple sources of digital elevation data sets
Users can subset and download data by area of interest in multiple formats and projections
Requires user registration via http://urs.earthdata.nasa.gov
Data can be previewed before downloading
http://gdex.cr.usgs.gov/

## Slide 17: SRTM V3 and ASTER DEM from GDEx
http://gdex.cr.usgs.gov/
30 m data

## Slide 18: SRTM V3 and ASTER DEM from GDEx
http://gdex.cr.usgs.gov/
Login with your NASA Earthdata username and password
Notes: Based on ~800 geodetic sites

## Slide 19: GDEx: SRTM Data Selection
http://gdex.cr.usgs.gov/
Zoom
Refresh
Download
Define region of interest by bounding box, state, country, or lat/lon
Notes: Based on ~800 geodetic sites

## Slide 20: SRTM Data from CGIAR-CSI
CGIAR-CSI: Consultative Group for International Agricultural Research Consortium of Spatial Information
http://csi.cgiar.org/WhtisCGIAR_CSI.asp
SRTM data (90 m)

## Slide 21: CGIAR-CSI: SRTM Data Access
Click to select and download data

## Slide 22: CGIAR-CSI: SRRTM Data Selection
Spatial selection can be by lat/lon
or by clicking on the grid(s)
Select data format
Clear Grid Selection

## Slide 23: CGIAR-CSI: SRTM Data Download
Download options
Digital elevation data can be downloaded as GeoTIFF

## Slide 24: GDEx and CGIAR-CSI
Both tools are easy to use with spatial subsetting
Data can be downloaded as GeoTIFF to import in GIS
GDEx SRTM is 30 m whereas CGIAR-CSI is 90 m
CGIR-CSI provides combined multiple tiles whereas GDEx provides a series of individual tiles
GDEx also provides access to ASTER GDEM2 and other DEM data
GDEx requires user registration and login through NASA Earthdata

## Slide 25: Next Demonstration of GDEx